## Slide 1: Blue-Light Filtering Spectacle Lenses: Optical and Clinical Performances
Team no: 5
Presented By
Sudirgha Chakma
ID: 22373002
Course Title: Cse713
Research Assistant: Adib Mahammad Amit
Student Tutor: Sadiul Arefin Rafi

## Slide 2: INTRODUCTION
Blue light is short-wavelength electromagnetic radiation (400–500 nm) in the visible spectrum (400–780 nm) that carries the highest amount of energy per photon. It has drawn increasing attention due to a hypothesis suggesting that blue light has the potential to induce photochemical damages to the retina.
The sun and artificial light sources, including LED (light-emitting diode) light bulbs and fluorescent light tubes, are the primary sources of blue light, emitting the amount of blue light that approaches the international exposure limit. With the increasing popularity of blue-rich LED-backlight display devices, such as mobile smartphones, ultraportable tablets, and computer screens, our eyes are exposed to more blue light than in the past

## Slide 3: PURPOSE
To evaluate the optical performance of blue-light filtering spectacle lenses and investigate whether a reduction in blue light transmission affects visual performance and sleep quality.

## Slide 4: METHODS
Experiment 1:
The relative changes in phototoxicity, scotopic sensitivity, and melatonin suppression of five blue-light filtering plano spectacle lenses were calculated based on their spectral transmittances measured by a spectrophotometer.
Experiment 2 :
A pseudo-randomized controlled study was conducted to evaluate the clinical performance of two blue-light filtering spectacle lenses (BF: blue-filtering anti-reflection coating; BT: brown-tinted) with a regular clear lens (AR) serving as a control. A total of eighty computer users were recruited from two age cohorts (young adults: 18–30 yrs, middle-aged adults: 40–55 yrs). Contrast sensitivity under standard and glare conditions, and colour discrimination were measured using standard clinical tests. After one month of lens wear, subjective ratings of lens performance were collected by questionnaire.

## Slide 5: RESULTS
All tested blue-light filtering spectacle lenses theoretically reduced the calculated phototoxicity by 10.6% to 23.6%. Although use of the blue-light filters also decreased scotopic sensitivity by 2.4% to 9.6%, and melatonin suppression by 5.8% to 15.0%, over 70% of the participants could not detect these optical changes. Our clinical tests revealed no significant decrease in contrast sensitivity either with 95% confidence intervals or without glare and colour discrimination.

## Slide 6: FUTURE WORK
Although there hasn't been much research done on the effect of blue light blocking glasses, some studies show that blue light glasses may:
Improve visual performance.
Improve sleep quality.
Alleviate eye fatigue.
Conserve macular health.

## Slide 7: CONCLUTION
Blue-light filtering spectacle lenses can partially filter high-energy short-wavelength light without substantially degrading visual performance and sleep quality. These lenses may serve as a supplementary option for protecting the retina from potential blue-light hazard.